Reconstruction of charge number of heavy cosmic rays using Cherenkov Light
Robert Stein, Attila Abramowski, Dieter Horns

---
Lateral Photon Distribution Method
- New reconstruction method, fitting received DC photons to known Lateral Distribution Function.
- Aim to improve reconstruction of Charge.

---
Fitting and event reconstruction
- Five variables to reconstruct:
  - x/y Core Position,
  - First Interaction Height,
  - Energy per Nucleon
  - Charge.

---
Likelihood
P_{i} ( N_{i, Received} divides X, Y, Z, height, Epn ) = { func e^{- %lambda_{i} } times %lambda_{i} ^{N_{i}} } over { fact {N_{i}} }
ln( fact {N} ) approx N ln(N) - N + {1} over {2} ln(2 %PI N)
- ln(L) = - sum from{i} ln( P_{i}) = sum from{i} %lambda _{i} - N_{i} ln(%lambda _{i}) + N_{i}ln(N_{i}) - N_{i} + {1} over {2} ln(2 %PI N_{i})

---
Iterative Minimisation
- Fix Z at integer value (Range Z=20-32)
- Use a ~3x3m grid of points in 200m x 200m area
- Select all points within reconstruction target (~10)
- Iteratively minimise over valid 20 Epn x 3 Height starting combinations for each location (~51)
- Run 13 x 10 x 51 = 6630 minimisations
- Select minimisation candidate with lowest resultant log likelihood as overall minimum

---
Optimised Telescope Array
- Grid of nine large telescopes (12m Diameter)
- Expected counts for 50 hours run time
- Count rate for many-telescope events improves with small grid spacing
- Reconstruction accuracy for individual images improves with large spacing to cover entire lateral distribution
- Minimise σZ by balancing competing effects

---
Summary
- New Technique for Charge Reconstruction, valid for both current and future IACT systems.
- Simulation with HESS-type layout yields a much improved core reconstruction.
- Charge resolution of σZ < 0.3 for five telescope events.
- Ideal future CT experiment would have 9 telescopes with a grid spacing of ~20-40m.
- Consequent event rate would be ~15 events per hour observed by 5 or more telescopes.