Reconstruction of charge number of heavy cosmic rays using Cherenkov Light
Robert Stein, Attila Abramowski, Dieter Horns
Universität Hamburg
DPG-Frühjahrstagung 2016

---
Aim of the analysis
- Cosmic Rays Cherenkov Light is imaged by telescopes eg. HESS
- Events currently reconstructed with Hillas Analysis
- However Core position/Charge resolution is poor

---
Lateral Photon Distribution Method
- New reconstruction method, fitting received DC photons to known Lateral Distribution Function.
- Aim is to improve reconstruction of Charge.

---
Fitting and event reconstruction
P_{i} ( N_{i, Received} divides X, Y, Z, height, Epn ) = { func e^{- %lambda_{i} } times %lambda_{i} ^{N_{i}} } over { fact {N_{i}} }
- Five variables to reconstruct:
  - x/y Core Position,
  - First Interaction Height,
  - Energy per Nucleon
  - Charge.
+
ln( fact {N} ) approx N ln(N) - N + {1} over {2} ln(2 %PI N)
- ln(L) = - sum from{i} ln( P_{i}) = sum from{i} %lambda _{i} - N_{i} ln(%lambda _{i}) + N_{i}ln(N_{i}) - N_{i} + {1} over {2} ln(2 %pi N_{i})

---
Iterative Minimisation
- Iterate over integer Z
- Select a ~100m² region
- Scan valid Height/Energy combinations
  - 13 Z values
  - 10 positions
  - 51 Epn/Height Combos
  - 13 x 10 x 51 = 6630
Candidate with smallest log likelihood of the 6630 runs is selected

---
Optimised Telescope Array
X
- Grid of 3 x 3 telescopes (variable grid width X)
- Expected counts for 50 hours run time
- Minimise σZ by balancing competing effects
X

---
Summary
- New Technique for Charge Reconstruction, valid for both current and future IACT systems.
- Simulation with HESS-type layout yields a much improved core reconstruction.
- Charge resolution of σZ < 0.3 for five telescope events.
- Ideal future CT experiment would have 9 telescopes with a grid spacing of ~20-40m.
- Consequent event rate would be ~15 events per hour observed by 5 or more telescopes.