Reconstruction of charge number of heavy cosmic rays using Cherenkov Light
Robert Stein, Attila Abramowski, Dieter Horns

---
Fitting and event reconstruction
  - We need to determine x, y, height, Z and Epn
- Five variables, but with constraints...
  - Z is always an integer
  - Non-hits for telescopes provide location information
  - The energy must have been greater than the threshold for any chosen height.
  - The images provide additional information, used to efficiently sample likely positions for reconstruction

---
Likelihood
P_{i} ( N_{i, Received} divides X, Y, Z, height, Epn ) = { func e^{- %lambda_{i} } times %lambda_{i} ^{N_{i}} } over { fact {N_{i}} }
ln( fact {N} ) approx N ln(N) - N + {1} over {2} ln(2 %PI N)
- ln(L) = - sum from{i} ln( P_{i}) = sum from{i} %lambda _{i} - N_{i} ln(%lambda _{i}) + N_{i}ln(N_{i}) - N_{i} + {1} over {2} ln(2 %PI N_{i})

---
Repeated Minimisation
- Fix Z at integer value (Range Z=20-32)
- Use a ~3x3m grid of points in 200m x 200m area
- Select all points within reconstruction target (~10)
- Iteratively minimise over 20 Epn and 3 Height starting values for each starting location
- Run 13 x 10 x 20 x 3 = 7800 minimisations
- Select minimisation candidate with lowest resultant log likelihood as overall minimum

---
Summary
- New Technique for Charge Reconstruction, valid for both current and future IACT systems
- Simulation with HESS-type layout yields a much improved core reconstruction
- Resultant charge resolution of σZ < 0.3